## Slide 1: Basic Image Analysis (using ImageJ/FIJI)
Christian “Tischi” Tischer
tischitischer@gmail.com
Advanced Light Microscopy Facility (ALMF)
European Molecular Biology Laboratory (EMBL), Heidelberg, Germany

## Slide 2: Why ?
Fiji is just ImageJ (bundled with many Plugins)
Free, open-source, wide-spread
Visualization, analysis, automated analysis, 2-D and 3-D
Best software for interactive image inspection and analysis
However, complex workflows and batch analysis require scripting…

## Slide 3: Other free, open-source software
Batch analysis of 2-D data
Good object-logic
Dedicated to batch analysis with 2-D cell-classification and tracking
Does not support intensity quantification
3-D pixel- and object-classification and tracking
Batch analysis?

## Slide 4: ImageJ/Fiji Installation
Download from internet: http://fiji.sc/
Recommendations:
  For Windows don’t install in the Program Files folder but rather have the Fiji.app folder on the Desktop (due to User rights issues)

## Slide 5: An image is a matrix of numbers
8-bit: 0,1,..,255 (2^8 - 1)
12-bit: 0,1,..,4095 (2^12 - 1)
14-bit: 0,1..,16383 (2^14 - 1)
16-bit: 0,1,..,65535 (2^16 - 1)
Lookup Table (LUT)
“Grays”
“Green”
“Fire”

## Slide 6: Image data inspection
Image analysis starts on the microscope! The reason is that you can only later analyze images that have been acquired properly.
Acquiring images on the microscope you have to make many decisions, such as choosing an exposure time and a detector gain; taking those decisions you need to know how a “good” image should actually look like.
We will learn now what the criteria for a good image are and also learn about different ways and tools to check for those criteria.
We will start with a white-board session on
  Bit depth
  Saturation
  Offset
  Dynamic range
Also very important in this context is the concept of a signal to noise (S/N) ratio, which we will cover later.

## Slide 7: Image data inspection
Open “../image-inspection/A.tif” (File..Open)
Also open B.tif, C.tif, D.tif, E.tif
Use below methods (M1,M2,M3) to answer Question 1
M1: Adjust the display (Image..Adjust..Brightness/Contrast)
M2 :Examine gray values in whole image (Analyze..Histogram)
M3: Analyze gray values along a line (Analyze..Plot Profile)
Question 1:
which of the images is best described by:
no_problem, high_offset, low_offset,
low_dynamic_range , or saturation ?
Optional Task 2: modify the good_dynamic_range image such that it contains the same values as the high_offset image (Process..Math )
Optional Task 1: find (up to five) different ways of checking whether an image contains saturated pixels
Optional Task 1:
Mouse Over
Line Profile
Histogram
HiLo Lookup Table
Image..Transform..Image to Results
Optional Task 2:
divide by 2
add 120
Mention:
Image..Transform..Image to Results
Notes: Related functionality: [Image..Transform..Image to Results]; [Analyze..Tools..Calibration bar]
Optional Task 1: Answers: Mouse Over, Line Profile, Histogram, HiLo LUT, Image..Transform..Image to Results
Optional Task 2: divide by 2 and then add 120
7

## Slide 8: Image data presentation
The first step in any project involving image analysis is to visually inspect the images to see if they are actually worth analyzing.
For example, often one wants to see whether a certain treatment caused an effect. For this it is very important to show the treated and non-treated images in the most quantitative and also in exactly the same way.
The following practical will show you how to generate a good image data presentation.

## Slide 9: Image data presentation
[Analyze > Tools >
Scale Bar]
[Analyze >
Tools >
Calibration Bar]
[Image > Adjust > Brightness&Contrast]
- [Set] “Propagate to all
other open images”
Negative
control
Positive
control
Open all files in “../image-presentation” and try to generate below images, using the indicated Fiji commands
[Image > Color > Merge Channels]
To put the images into a PowerPoint presentation use:
[ Edit > Copy to System] and then simple paste (CTRL+V) them into PowerPoint

## Slide 10: Image format conversion
Unfortunately, quite often, it is necessary to convert an image from one format into another, e.g. because certain applications can only read certain formats
During such conversions many (bad) things can happen to the quantitative information in your image.
It is thus of critical importance to always test the image content before and after you saved it in another format.

## Slide 11: Image format conversion
open “../image-format-conversion/16bit.tif” (File..Open)
Adjust the display that you actually see something
adjust Jpeg quality (0-100) to 10 (Edit..Option..Input/Output)
save as Q10.jpg (File..Save As..Jpeg)
repeat the last 3 steps for Jpeg qualities 75, and 100
save as im.png (File..Save As..PNG)
adjust the display such that it appears saturated (Image..Adjust..Brightness/Contrast)
save as Q100_saturated.jpg (File..Save As..Jpeg)
save as im_saturated.png (File..Save As..PNG)
Q10.jpg
Q75.jpg
Q100.jpg
im.png
Task 1: compare the sizes of these files!
Task 2: compare the content of the images! (you have to re-open the saved images!)
Q100_saturated.jpg
im_saturated.png
Notes: Note: every year the outcome of this practical changes, showing how dangerous it is to save images in different formats (if you still want to quantify them).

## Slide 12: Image bit depth conversion
You should avoid it at all cost, but sometimes to have to convert images from one bit depth to another, e.g.
  Some old algorithms only work on 8-bit data
  You need to save hard-disk space
  You don’t have enough RAM to process you images in 16bit
During such conversions the gray values in your image are likely to be affected and you really have to make sure that you are in control about these changes, ensuring that you do not distort the scientific information in your data.
In the following we will discuss 16bit to 8bit conversion in general and in particular how ImageJ handles this.

## Slide 13: Image bit depth conversion discussion
What are sensible ideas for converting images from 16 to 8 bit?
  MinMax Bit-depth mapping
  MinMax image content mapping
  User adjusted mapping

## Slide 14: Conversion to 8-bit format
Open “../bit_conversion/16bit.tif”
examine the gray values using for instance: Analyze..Histogram or Analyze..Plot Profile
Duplicate the 16bit image (Image..Duplicate) perform the next steps on the duplicated image!
change display using: Image..Adjust..Brightness/Contrast..Set
convert to 8-bit: Image..Type..8-bit
Examine gray values of 8-bit converted image, using for instance: Analyze..Histogram or Analyze..Plot Profile
Take home message: ImageJ uses the Minimum and Maximum display values and, when converting to 8bit, maps those to 0 and 255.
Notes: Answer 1: The minimum displayed value will be set to 0 and the maximum displayed value will be set to 255 in the final 8 bit image.
Answer 2: There is no easy answer => better avoid conversions!

## Slide 15: Measurements in images
These days, for scientific publications, it is typically not enough to just show “representative images” but you need to provide measurements and statistics!
In the following we will practice a simple way to extract meaningful numbers from images.

## Slide 16: Manual measurements in multiple regions
open “../bit-conversion/16bit.tif”
draw region for Nucleus 1 as shown below using the Polygon Selection
save the region (Analyze..Tools..ROI Manager..Add)
name the region “Nucleus 1” (Analyze..Tools..ROI Manager..Rename)
Repeat above steps for Background and Nucleus 2
select “Mean Gray Value” measurement (Analyze..Set Measurements)
Select all regions and measure (ROI Manager…Measure)
Nucleus 1
Nucleus 2
Background
Question: how much brighter is nucleus 1 than nucleus 2?
Optional Task: measure the area of all nuclei (which one is the largest)?
Notes: Useful: [ROI Manager..More..Labels] => shows the names on the image

## Slide 17: Measuring signal to noise in images
Sitting on the microscope, you have to decide on many settings, including excitation intensity and exposure time.
Typically you need to balance photo-toxicity and bleaching with image quality.
In this context, image quality typically means “signal to noise ratio” (S/N). This is important, because if the S/N is too low, it will be difficult to detect your objects of interest and even more difficult to properly measure their intensity.
Here, we will learn how to measure S/N in an image.

## Slide 18: Measuring signal to noise
Signal to Noise = (Mean(Object)- Mean(BG)) / Sqrt(Sdev(Object)^2
Nucleus 1: 4.7
Nucleus 2: 2.0
Signal
BG
Noise
Signal
Noise
Signal
Noise
Nucleus 1
Nucleus 2

## Slide 19: Measure signal to noise
[File > Open] “../signal-to-noise/h2b-mcherry.tif”
[Analyze > Set Measurements] “Mean gray value”, “Standard deviation”
Draw region as shown using the “Oval Selection”
Save region [Analyze>Tools>ROI Manager>Add]
Name region [Analyze>Tools>ROI Manager>Rename]
Select all regions and measure [ROI Manager>Measure]
Apply below formula to measure a S/N ratio: (Mean(Signal)-Mean(BG)) / Sqrt(Sdev(Signal)^2 + Sdev(BG)^2)
Notes: Answer 1: The minimum displayed value will be set to 0 and the maximum displayed value will be set to 255 in the final 8 bit image.
Answer 2: There is no easy answer => better avoid conversions!

## Slide 21: multi-color and scale-bar
open all images in “../multi-color/” [File..Import..Image Sequence]
convert to a “Composite Image” [Image..Color..Make Composite]
open the “Channels Tool”: [Image..Color..Channels Tool]
change channel colors [Image..Lookup Tables..]
  you have to move the channel slider (see screenshot below)
change scaling to 0.16 um [Image..Properties]
add scale bar [Analyze..Tools..Scale Bar]
  Activate the Overlay checkbox
save image twice:
  [File..Save As..Tiff]
  [File..Save As..Jpeg]
open both in PowerPoint and compare
reopen both in Fiji and compare
Optional task 1: try making the nucleus appear brighter and the microtubules dimmer
slider to select active channel!
Aim: the image should look like this
Notes: Task 1: select the respective channel and change appearance with [Image..Adjust..Brightness/Contrast]

## Slide 22: always keep your raw images! (do conversions only on duplicates!)

## Slide 23: Biological interpretation of intensity measurements
Intensity measurements are a difficult thing, because there are many (technical) factors that can influence the intensity in an image. This topic is almost another course and should be (also) taught at the microscope…
In addition, even if microscopy and sample preparation were performed perfectly (settings, controls, etc…), and you saved your images properly, one still needs to understand what a certain intensity readout means!
=> Whiteboard session (or show slides from other talk) on difference between widefield vs. confocal acquisition and mean vs. total (sum) intensities.

## Slide 24: 16-bit (or 8-bit) vs. 32-bit images
open “../bit-conversion/16bit.tif” [File>Open..]
Duplicate raw data [Image>Duplicate..]
Subtract 800 gray [Process>Math>Subtract..]
  Compare gray values before and after subtraction! Do you observe something mathematically wrong?
Duplicate raw data [Image>Duplicate..]
Divide by 2 [Process>Math>Divide..]
  Compare gray values before and after subtraction! Do you observe something mathematically wrong?
Check how above subtraction and division changes when you convert the image to 32-bit beforehand [Image>Type>32-bit]
Take home message: before doing any math to your image, convert to 32bit

## Slide 25: Manual background subtraction on an image
Open “../bit_conversion/16bit.tif”
Convert image to 32-bit: [Image..Type..32bit]
  This allows for negative numbers in the image
Draw ROI in the BG
  Increase brightness a lot to see whether it really is BG
Select measurement “Mean Gray Value” [Analyze..Set Measurements]
Measure BG intensity [Analyze..Measure]
Remove the BG ROI [Edit..Selection..Select None]
Subtract BG intensity [Process..Math..Subtract]
Put back BG ROI [Edit..Selection..Restore]
Now measure BG intensity again [Analyze..Measure]
  You should get zero 
Repeat everything but leave the image 16bit (do not convert to 32bit)
  The resulting BG intensity should not be zero 
Notes: You have to remove the BG ROI before the subtraction, because otherwise ImageJ only subtracts the value from this region.
If you don’t convert to the image to 32bit there can be no negative numbers and thus the background subtraction does not work properly…

## Slide 26: Threshold and automated particle analysis
open image “../dynamic-range/B.tif”
  Select the measurements you want to extract (e.g., “Area” and “Shape descriptors”):
  [Analyze..Set Measurements]
Threshold the image (Image..Adjust..Threshold)
  Only move the upper slider (lower should be on 255)
  Do NOT press Apply; simply leave the Threshold dialog open
Detect & measure the objects (Analyze..Analyze Particles)
  “Show: Overlay Outlines”
  “Select: Display Results”
Question 1: what is the average size of the nuclei?
Question 2: how can you exclude nuclei that are not fully in the image?
Optional Task 1: Examine the Results table and find values for the Size- and Circularity-Filter in Particle Analyzer such that some Nuclei are excluded.

## Slide 27: Point Spread Function Examination
Open “../psf/beads_p_close.tif” (File..Open)
  Hyperstack: two channels: green (c1) and red (c2) bead
Generate side views (Image..Stacks..Reslice)
  Do NOT avoid interpolation
Project into 2-D (Image..Stacks..Z-Project)
  Projection Type: Sum Slices
Repeat above steps for “../psf/beads_p_open.tif”
Question: What is the difference between open and closed pinhole?
Optional Task 2: Generate above movie
- File..Open
Image..Color..Split channels
Image…Lookup Tables..Fire
- Image..Stacks..3D Project (interpolate)
Optional Task 1: Compare the apparent width of green and red bead (in the xy-direction). Choose a central z plane in the original file and:
Analyze..Plot Profile
Analyze..Tools..Curve Fitting (gaussian)
- copy the list from the profile plot into the fitting tool
This is a “hyperstack”,
containing a channel-
and a z-slider
Notes: Optional Task 1:
27

## Slide 28
Point Spread Function Examination: Results

## Slide 29: Measuring FRAP data (also uses a macro)
bg
signal
bleach
ref
bg
ctrl
Question: What is the recovery half-time of the signal?
(estimate it from the final graphs; dt=2s)
Optional Task: Modify the macro such that it only shows the raw bleach curve without normalizations.
open all files in “../frap/” (File..Import..Image Sequence)
draw 4 regions as shown and add them to the ROI manager (Analyze..Tools..ROI Manager..Add)
  Rename them (it is important that they have the exact names: bleach, ref, ctrl, bg )
Select only the “Mean Gray Value” measurement (Analyze..Set Measurements)
Select all regions and measure (ROI Manager…More>>…Multi Measure)
Open “../Macros/Macro_bleaching.ijm” (drag and drop onto FIJI) and Run the Macro
*
*
*
*
Notes: You can also load ROIs from images, if they are saved inside the image format: Example: open “../LOCI/Arf1-GFP_Golgi_FRAP.oib” and check “Display ROIs”

## Slide 30: Examine 3-D data using Hyperstacks and 3-D Viewer
open “../4D/mitosis_tub-h2b.lif” as Hyperstack (Plugins..LOCI..Bioformats Importer)
  examine data using Hyperstack sliders
Separate channels: Image..Color..Split Channels
  Alternatively keep both channels: Image..Color..Make Composite
Select DNA channel and open volume view (Plugins..3D Viewer)
  accept default values
Examine data by
  Rotating (left mouse button)
  Zooming (mouse wheel)
  Playing the movie
Change Display Settings
  Edit...Change Color
  Edit...Transfer Function
Question: what do you notice when viewing chromosomes from the side?
Optional Task 1 (if your computer is strong enough…): open “../zebrafish_wholefish_neurons.tif”
and/or “../egg-chambers_3d.lsm”
make movie (3D Viewer: View..Record 360 deg rotation)
save movie (File..Save As..Avi)
Notes: 30

## Slide 31: Colocalisation
One often is interested whether two proteins are localized on the same intracellular compartment.
The quantification of such “co-localization” images is not trivial and there exist many methods.
A good review is: Journal of Microscopy, Vol. 224, 2006, pp. 213–232. A guided tour into subcellular colocalization analysis in light microscopy. S. B O LT E & F. P. C O R D E L I È R E S
In the following we will only discuss pixel/object based co-localisation measurements (as these are the easiest to interpret).
HeLa cells with two proteins of the secretory pathway in conditions where the Golgi is fragmented. (Christian Schuberth, EMBL)

## Slide 32: Pixel based co-localization
Open “../colocalisation/1_GalNAc-GFP” and “../colocalisation/1_AB2-COP1”
Threshold the two individual images (Image..Adjust..Threshold)
  Check Dark background
  Click Apply
Divide images by 255 to set object pixels to 1 (Process..Math..Divide)
Create co-localization image by multiplying the two images (Process..Image Calculator..Multiply)
Measure overlap:
  Select measurement “Integrated Density” (Analyze..Set Measurements)
  Measure all 3 images (Analyze..Measure)
    RawIntDen gives you the number of object pixels
Divide the number of objects pixels of the overlap image by either image 1 or image 2 to get the respective co-localizations
Question 1: what is the co-localization of 1_GalNAc-GFP with 1_AB2-COP1?
Question 2: what is the co-localization of 1_AB2-COP1 with 1_GalNAc-GFP ?
Optional Task 1: also examine the images 2_GalNAc-GFP and 2_AB1-LAMP1
Optional Task 2: Create color overlay (Image..Color..Merge Channels)
  Check Create Composite
  Use Green and Magenta
  Adjust brightness of both channels (Image..Adjust..Brightness/Contrast)

## Slide 33: Image filtering
Intensity threshold
Raw data
Enhance raw data
Objects
Intensity measurements

## Slide 34: White-board session on: Image filtering
Local pixel neighborhood
Mean smoothing
Gaussian smoothing
Median smoothing

## Slide 35: Image filtering for improved particle detection
Open image “../noisy_nuclei/noisy_nuclei.tif”
Threshold the image [Image..Adjust..Threshold]
Detect [Analyze..Analyze Particles]
  “Show: Overlay Outlines”
As you can see, this does not work very well…
Now, first smooth the image: [Process..Filters..Median] (Radius 7 pixels) and repeat the thresholding and particle detection
Optional Task 1: Work with the raw data (not smoothed) and try to improve the results with the “Size” exclusion and “Include holes” options of the Particle Analyzer.

## Slide 36: Top-hat filter
Quite advanced, but very useful as it both
enhances locally bright structures
performs a local background subtraction

## Slide 37: Top-hat filter removes local background and thereby enhances locally bright structures
raw
erosion (local minimum, r=7)
dilation (local maximum, r=7)
tophat = raw - dil(ero(raw))
tophat & threshold
raw & threshold
GalNac-YFP Golgi precusors in BCS1 karyoplast (Gayathri Vegesna, EMBL Heidelberg)
“Background”
Image

## Slide 38: Top-hat filtering
Open “../top-hat/images/20X_GFP-slice51.tif”
Rename to “raw” (Image..Rename..)
Duplicate the image and call it “open” (Image..Duplicate..)
Perform an opening filter: open(raw)=dilation(erosion(raw)]
  Erode the image with a minimum filter of radius 7 pixels (Process..Filters..Minimum)
  Dilate the result with a maximum filter of radius 7 pixels (Process..Filters..Maximum)
Perform top-hat filter: tophat = raw-open(raw)
  Subtract the opened image from the raw image (Process..Image Calculator..)
  Rename the resulting image to “tophat” (Image..Rename..)
Compare thresholding vesicles in the “raw” and “tophat” image (Image..Adjust..Threshold)
Question 1: what is the difference between the raw image and the top-hat filtered image?
Question 2: what happens if the radius of the opening filter is very small (e.g. 1 pixel) (try it!)
Question 3: what happens if the radius of the opening filter is very large (e.g. 100 pixel) (try it!)
top-hat & threshold

## Slide 39: Distinguishing dots from lines
Draw line and dot (pixel width =3)
Plugins..Feature Extraction..FeatureJ
  Hessian

## Slide 40: Image segmentation (object detection) using supervised machine-learning
Intensity threshold
Raw data
Enhance raw data
Objects
Intensity measurements
X

## Slide 41: Supervised machine learning
In a nutshell: The computer computes many (~100) filters on each image and learns how to combine them to find your objects of interest

## Slide 42: White-board session on supervised pixel classification
Feature vectors
Labeling
Learning

## Slide 43: Supervised automated pixel classification
Open “../supervised_segmentation/scanningEM_flyEye.tif”
Run [Plugins..Segmentation..Trainable Weka Segmentation]
Add labels using the freehand line tool:
  mark regions on the eye [Add to class 1]
  mark regions outside the eye [Add to class 2]
Try the prediction: [Train classifier]
Add more labels to regions where the prediction is not yet satisfactory
If you are satisfied export results: [Get probability]
Use thresholding [Image..Adjust..Threshold] and the particle analyzer [Analyze..Analyze Particles] to segment the eye
Freehand line tool
Trainable Segmentation

## Slide 44: Stitching with flat-field correction
Open “../stitching/…”
Open “../stitching/..” **
Flat-field correction of all images:*
Smooth flat-field image [Process>Filters>Mean](radius: 5)
Measure mean intensity of the flatfield image [Analyze>Measure]
Divide all images by the smoothened flat-field: [Analyze>Tools>Calculator plus]
  i1: tiles_3x3_10%overlap.lsm; i2: flatfield; k1: mean intensity of flat-field image; k2: 0
Select the result and [File>Save As>Image Sequence](Name: tile_)
Stitching of corrected images:
[Plugins>Stitching>Grid/Collection stitching](click OK)
  Grid size x & y: 3
  Tile overlap: 10
  First file index: 0
  Directory: Choose the directory where you saved the tiles
  File names for tiles: tile_{iiii}.tif
* here we assume that pixel intensities in the absence of a sample are zero; if this is not the case you have to subtract the non-zero offset from all images before doing the flat-field correction.
** computing a flat-field from the tiles can be quite good (for sure better than the fluo-slide)

## Slide 45: Flat-field correction
5x5 stitched raw
5x5 stitched corrected

## Slide 46: Time-lapse handling and analysis

## Slide 47: Time-lapse: Movie making and annotation
Open “../tracking/ TransportOfEndosomalVirus.tif”
Add time information: [Image..Stacks..Time Stamper] (dt=2s)
Save as movie: [File..Save As..AVI…] (jpeg compression)

## Slide 48: Manual Tracking
Open “../tracking/ TransportOfEndosomalVirus.tif”
Start tracker: [Plugins..Tracking..Manual Tracking]
Enter scaling [Check: Show Parameters]
  Time interval: 2 s
  x/y calibration: 0.129 um
Track a few (e.g., 3) different particles
  [Check: Use centering correction? Local Maximum]
  Track particles: [Add track] click..click… [End track]
Try the different drawing options, e.g. [Overlay Dots & Lines]
Examine the results table: what are the fastest speeds that you measured?
Notes: it is handy to magnify the movie before you start tracking
while adding tracks, click nowhere else!
velocity of Kinesin inside HeLa cells = 0.6 µm/s
a handy “trick” to see all areas visited by the vesicles is to perform a “Maximum intensity projection” [Image..Stacks..Z Project] (Maximum Intensity)

## Slide 49: Kymograph Analysis
Open “../gfp_tirf_dt0.5s_dx106nm.TIF” (File..Open)
Enhance microtubules (Process..Subtract Background)
  5 pixel radius (no “light background”)
Trace a dynamic microtubule (Segmented Line Tool)
  Optional Trick: Make a max-projection of the movie
Change scaling to 1 pixel in x,y and z (Image..Properties)
Make Kymograph (Image..Stacks..Reslice)
  Accept all default values
Task: measure one growth and one shrinkage speed of a microtubule (see example below). dx_pixel = 106 nm, dt_pixel = 0.5 s
Demonstrate: segmented line, save as x-y coordinates…
dx= -35 pixel
dt= +7 pixel
space x
time t
Notes: Optional Task 1:
49

## Slide 50
Chart: Time (s)
| 0 | 5.5 | 7 | 12 | 16.5 | 28 | 32 | 38 | 42.5 | 45 | 47.5 | 51.5 | 58.5 | 60 | 60.5 | 68.5 | 75 | 82 | 82.5
 | 7.844 | 8.374 | 7.314 | 8.374 | 8.904 | 9.116 | 5.3 | 6.678 | 6.996 | 7.314 | 6.89 | 7.42 | 7.42 | 7.314 | 6.042 | 7.526 | 7.632 | 1.59 | 1.166
segmented line, save as x-y coordinates…
Kymograph Analysis Results

## Slide 51
Automated Tracking
Kota Miura EMBL, Heidelberg
Thomas Pengo CRG, Barcelona
Christian Tischer EMBL, Heidelberg

## Slide 52: White-board session on: Automated tracking
Linkage costs:
  Local
  Global
  Distance
  Morphology
Birth and death costs
Gap costs
Split and merge costs
t
t+1
t
t+1
t
t+1
t
t+1
t
t+1
t+2
t
t+1
t+2

## Slide 53: Automated Tracking: Installing a Tracking Plugin
Install the “MOSAIC Particle Tracker”
  Feature point tracking and trajectory analysis for video imaging in cell biology. I.F. Sbalzarini, P. Koumoutsakos, Journal of Structural Biology 151 (2005) 182–195
[Help..Update Fiji]
  Click: Manage Update Sites
  Check: MOSAIC ToolSuite and click Close
  Click: Apply Changes
After restarting you should now have: [Plugins..Mosaic..Particle Tracker 2D/3D]

## Slide 54
Automatic Tracking
Radius: Estimate of particle radius
Cutoff: “Non-particle” discrimination Percentile: Particle brightness in upper xx % of histogram
Exercise
Load “../tracking/TransportOfEndosomalVirus.tif”
[Plugins..Mosaic..Particle Tracker 2D/3D]
‘Preview’ with different parameters.
Questions:
What happens if you set the “radius” very large (e.g., 10)?
What happens if you put the “percentile” very high (e.g., 1)

## Slide 55
Automatic Tracking
Displacement: maximum distance of movement between frames
Link range: number of following frames to be considered for linking

## Slide 56
Automatic Tracking
Radius: 3
Cutoff: 0
Percentile: 0.6
Link range: 3
Displacement: 20
‘OK’
‘Visualize all trajectories’

## Slide 57
Automatic Tracking
Try entering some values!
50
100

## Slide 58
Automatic Tracking
Click ‘Focus on Selected Trajectory’
Select a track, and then..
Click ‘Focus on Area’

## Slide 59
Automatic Tracking
‘All Trajectories to Table’
Excel, ImageJ Macro,
Matlab, R, …

## Slide 60
Automated Tracking
and cell classification
=> Cellcognition

## Slide 61
3-D visualisation
Open “../3D_segmentation/primordium.tif”
Ortho-slicing [Image..Stacks..Orthogonal views]
3D Viewer:
  Start 3-D Viewer: [Plugins..3-D Viewer]
  Rotate (Click and move)
  Zoom (PC: mouse wheel; Mac: Two fingers)
  Pan: shift-drag

## Slide 62: 3-D segmentation and object analysis (using supervised learning)
Open “../3D_segmentation/primordium_crop.tif”
Convert to RGB [Image..Type..RGB color]
Train the “cell” and “non-cell” classes using [Plugins..Segmentation..Trainable Weka Segmentation]
  When satisfied click “Get probability”
Extract the “cell channel” (Channel 1): [Image..Stacks..Tools..Make Substack]
Smooth the probability map: [Process..Filters..Gaussian Blur…] (radius: 2 pixels)
Convert to 8bit [Image..Type..8-bit]
[Analyze>3D objects counter]
  Play with the settings and output options
  ..3D OC options (chose the image to compute intensities on…)
Combine “Surface Map” with the raw data [Image..Color..Merge Channels]
How many cells did you find?

## Slide 63: ImageJ Macros
If a certain analysis procedure consist of many steps it is convenient to “record” them and apply them automatically at once.
To do so, ImageJ Macros are a great tool

## Slide 64: Tophat filtering macro
Open “../top-hat/images/20X_GFP-slice51.tif”
Turn on Macro Recorder (Plugins..Macros..Record)
Rename to “raw” (Image..Rename..)
Duplicate the image and call it “open” (Image..Duplicate..)
Perform an opening filter [open(raw)=dilation(erosion(raw)]
  Erode the image with a minimum filter of radius 7 pixels (Process..Filters..Minimum)
  Dilate the result with a maximum filter of radius 7 pixels (Process..Filters..Maximum)
Perform tophat filter [tophat = raw-open(raw)]
  Subtract opened image from raw image (Process..Image Calculator..)
In the Macro Recorder click Create and clean up the code to look like this:
  rename("raw");
  run("Duplicate...", "title=open");
  run("Minimum...", "radius=7");
  run("Maximum...", "radius=7");
  imageCalculator("Subtract create", "raw",“open");
Open “../top-hat/images/20X_GFP-slice51.tif”
Execute your macro (In the macro window: Run..Run)

## Slide 65: Batch Analysis
Often you want to apply the same sequence of analysis steps to a bunch of different images: this is called “Batch Analysis”
In the following, we will explore some ways how to do this in ImageJ

## Slide 66: Batch analysis using macros: Top-hat filtering of many images
Open: [Process..Batch..Macro]
As input choose: “..Macros\batch_tophat\input_data\ “
As output choose: “..Macros\batch_tophat\output_data\ “
Copy and paste the top-hat macro code
Run it by clicking: Process
Inspect the output folder

## Slide 67: Batch analysis using image stacks: Top-hat filtering
Many ImageJ commands work on stacks; so an alternative workflow for batch-processing of many images can be
  load all your images via “File..Import..Image Sequence”
  perform the image processing on the image stack
  Save to individual files via “File..Save As..Image Sequence”
For instance, try the top-hat filtering on the images in “..Macros\batch_tophat\input_data\”

## Slide 69
Things to add:
Deconvolution?
  Is it intensity preserving?
Stackreg
  Try on a mitocheck movie
Sum and Max Projection
  What would be good data?
Advanced Intensity quantification
  Get the DNA damage data from the woman in the Copenhagen course
Macro programming:
  To the top-hat macro, add:
    Variable for radius
    Get User input from GUI
    Particle Analyzer